## Slide 1
Utah Division of Water Rights
June 21, 2004
Permitting & Regulation
Jim Goddard—April 2017
Water Wells

## Slide 2: Well Drilling Topics
The Well Drilling Situation in Utah
Well Permitting Mechanisms and Process
Well Renovation, Replacement, & Abandonment Process
Non-Production Well Permitting
Pump Installation Requirements
General Administrative Rules
General Construction Rules
Well Info On Our Website

## Slide 3: Utah Well Drilling Data
154 licensed well drillers, 134 Licensed Pump Installers, and 239 Registered Operators
882 Non-Production Wells last year (604 heat pump)
400 Production Wells last year (49% Air, 21% Cable Tool, 19% Mud)
  83% DOM/IRR/STK Wells
  7% Irrigation Wells
  5% Stockwater Wells
  3% Public Supply Wells
  2% Commercial/Industrial Wells
65% of water wells were 4-6 inch dia.

## Slide 4
Chart: Utah Wells Drilled by Year
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Production Wells | 967 | 962 | 720 | 603 | 622 | 682 | 604 | 417 | 350 | 291 | 331 | 367 | 357 | 405 | 400
Non-Production Wells | 254 | 385 | 851 | 1273 | 1245 | 1769 | 1830 | 1938 | 1080 | 1086 | 1800 | 1194 | 1920 | 650 | 882
http://www.waterrights.utah.gov/wellinfo/stats2k/default.asp

## Slide 5
Chart: Number of Production Wells Drilled by Year

## Slide 6: Common Utah Drilling Methods
Mud Rotary
Cable Tool
Air Rotary
  Down-hole Hammer
  Drill-through Casing Drivers
  Under-reamer Systems
  Dual Rotary
  Reverse Air Rotary
Flooded Reverse Rotary
Other Methods (Jetting, Direct Push, Sonic, Percussion Hammer, Hollow Stem Auger, Coring, Horizontal, Bucket Auger, etc.)

## Slide 7: Activity Permitting
Well Drilling

## Slide 8: Well Permitting Mechanisms
Application to Appropriate
Change Application
Exchange Application
Temporary Change Application
Provisional (Rush Letter)
Well Renovation
Well Replacement
Non-Production Well
  Test, Monitor, Cathodic, Heat Pump, Dewater, etc.

## Slide 9: Application Process New Water Production Wells
Approval (New, Change, Exchange)
  Application
  Review & Advertise
  Protest Period
  Hearing
  Memo Decision, Approval letter, Start Cards
  Durations varies (weeks to months…or longer)

## Slide 10: Well Drilling Fees
Fee is based on quantity of water right for Production Wells (see table)
No fee for Non-production well permits
No fee for permit to renovate and replace a well

## Slide 11
State Engineer’s
Water
Appropriation Policy

## Slide 12: Application Process
When and what forms are filed

## Slide 13: Application to Renovate
Application to Renovate An Existing Well
  Modification to well (deepen, liners, screens, perforations, casing repair, pitless, seal, etc.)
DOES NOT grant approval to replace
No Application fee
Title and ownership must be current
Allows for repair, renovation, and/or deepening
Need separate application to replace well

## Slide 14: When a Renovation Permit is Needed
Renovate Permit Needed
  Deepening
  Well Repair/Renovation
  Anytime the well itself is modified
Renovate Permit Not Needed
  Cleaning
  Development
  Disinfection
  Testing
  Pump Work
Still needs to be done by a licensed Driller or Pump Installer
Still need to submit a pump log to report this information

## Slide 16: Application for Well Replacement
“Application to Replace an Existing Well”
Replacement well must be within 150 feet of old well for this process
Over 150 feet goes to change application process
Owner responsible to have licensed driller abandon existing well
No Application fee
Title and ownership must be current
Abandonment of existing well a condition of approval
Well log and abandonment log are tracked and both must be returned by Driller

## Slide 18: Well Abandonment Process
To abandon means to seal the well bottom to top with approved sealing materials
A well must be abandoned by a licensed well driller
Temporary versus Permanent Abandonments
When a well is replaced, the old well must be abandoned as a condition of approval
For a stand-alone abandonment, a permit is not required
  However, Water Rights must be notified prior to abandonment by the licensed driller
The licensed driller submits a certified abandonment log to Water Rights which becomes part of the water right record

## Slide 20: Application for Non-Production Wells (NPW)
Types of wells included:
  Test Wells (No WR Application filed)
    Provisional (Rush) wells do NOT use this form
  Cathodic Protection Wells (>30')
  Closed Loop Heat Exchange Wells (>30')
  Monitor Wells (>30')
Approval to construct (NPW Form; No Fee)
  Given by Well Drilling and/or Regional Offices
  Up to 14-day review
  NPW Public Listing

## Slide 22: Provisional Wells A.K.A. “RUSH LETTER”
Permission to drill before WR-related application approved
Granted at owners risk
Authorization to drill, construct, and test, but not put into production or beneficial use
Linked to WR application and processed through WR database
Owner files application (e.g., new, change, exchange) first, then submits written request to start drilling
Requests reviewed and approved by Regional Engineer

## Slide 23
Utah Code Section 73-3-5(4) provides that the state engineer may issue a temporary receipt to drill a well at any time after the filing of an application to appropriate water therefrom... provided in the judgment of the state engineer there is unappropriated water available in the proposed source and there is no likelihood of impairment of existing rights.
Water right process must still be followed
Written request with or after WR application
Approval to drill, construct, and test, but cannot divert the well water or put to beneficial use until after the WR application has been approved

## Slide 24: Well Drilling Rules

## Slide 25: Administrative Rules for Water Wells R655-4 Utah Administrative Code
  “Provide order and certainty in the beneficial use of Utah’s water”

## Slide 26: Scope of Rules Regulated Wells/License Required
Production Wells Greater than 30 feet deep
  Permitted through WR Process in WR database and associated with a WR#
    Domestic
    Irrigation
    Stock
    Public supply
    Commercial/industrial
    Open Loop Heat Exchange Wells
    Well Renovation & Replacement
Non-Production Wells (NPW) greater than 30 feet
  Permitted through NPW process in well drilling database and associated with a NPW number (aka M00 #)
    Test Wells
    Monitoring Wells
    Cathodic Protection Wells
    Closed Loop Heat Exchange Wells
    Misc. Wells (Piezometers, inclinometers, anode)

## Slide 28: Wells Excluded from the Rules
Any well less than 30 feet
  IMPORTANT: Production wells less than 30 feet deep still need a Water Right
Geothermal Wells (Regulated by R655-1 UAC)
Exploratory or geotechnical borings
Structure monitoring wells if aquifer not impacted
Dewatering wells if aquifer not impacted

## Slide 29: “Well Drilling” Regulatory Definition
Well drilling means the act of drilling, constructing, repairing, renovating, deepening, cleaning, developing, or abandoning a well
Pump installation and repair is now regulated by the Rules

## Slide 31: Administrative Rules
License required for drillers and pump installers
  Experience, testing, bonding, continuing education, renewal
Registration required for rig operators
Violations, Infractions, and Enforcement
Removing Drill Rig from Site
Requirements During Construction
  Drill at approved location
  License No. or Company name on rig
  Licensed driller or registered operator on site
Reporting Requirements
  Start Card Submitted for starting regulated work
  Well log - 30 days after completion of well
  Specific log for each well
  Pump Logs
  Abandonment reports
  APPLICANT CARD

## Slide 33: Pump Installation Rules
License required of those doing work professionally for compensation
Doing own work on own property on own well does not require a license
No permits or start cards required
Required reporting to include a Pump Log

## Slide 35: Additional Permitting for Public Supply Wells
Regulated through the Division of Drinking Water (R309-515)
Project Notification
Preliminary Evaluation Report/Drinking Water Source Protection Plan
Preapproval of Plans/Specifications
  Drilling/Construction Materials and Methods
  Certified Sealing
  Pump Testing and Water Quality
  Disinfection
  Submitted by Licensed Driller, Professional Engineer, or Professional Geologist
  Fines for submitting this info after the fact

## Slide 36: Construction Requirements

## Slide 37: Main Components
Well Casing, Joints, Screens, & Perforations
Surface and Interval Seals
Formation Stabilizers – Gravel (Filter) Pack
Aquifer Protection (Fluids, Chemicals, LCMs, Cross-contamination, Disinfection)
Surface Completion
Special Wells & Monitoring Wells
Deepening, Rehab, and Renovation
Well Abandonment
Pump Installation and Repair

## Slide 38: Well Drilling Web Features www.waterrights.utah.gov

## Slide 39: QUESTIONS?
Jim Goddard
Office: 801-538-7314
Cell: 801-505-8677
Email: jimgoddard@utah.gov
Web: waterrights.utah.gov
“When the well is dry, we know the worth of water” …B. Franklin