## Slide 1: When is Water Not Wet?
Water Law and Policy Seminar
March 19, 2018
Jared Manning, P.E.
Assistant State Engineer

## Slide 2: Water Rights Quantification (“Currency” Units)
Early Days – Development of surface sources
  Irrigated Land (acres)
  Flow Rate (cfs)
Today – Development of wells
  Irrigated Land (acres), Livestock (elu), Domestic (edu)
  Diversion Volume (acre-feet)
  Depletion Volume (acre-feet)
Is flow rate relevant in today’s world?

## Slide 3: Distribution Duty
Early decrees assigned duties for surface water based on ac/cfs
Typical decreed duty is 40-120 ac/cfs; usually close to 60 ac/cfs
  1 cfs = 2 ac-ft/day
  (2 ac-ft/day * 30 days) / 60 ac = 1 ac-ft/ac/mo
  7 mo * 1 ac-ft/ac/mo = 7 ac-ft/ac
Duties today are mostly 3-5 ac-ft/ac
How is duty currently applied in distribution?

## Slide 4: Distribution Duty
Distribution is done by flow rate, not volume
  Exception #1: Duchesne/Strawberry Rivers
  Exception #2: Potentially Utah Lake
Normal irrigation season usually 5-6 months
Most primary rights reduced in the summer
Actual volume diverted about 2-5 ac-ft/ac

## Slide 5: “Carrier Water”
Definition: water diverted at the head of the canal that does not get applied to the land; or system inefficiencies
Examples
  Losses from seepage and evaporation
  Flow-through water past the last turnout
  Periodic Overflow
Reducing inefficiencies
  Canal lining, piping
  Storage ponds
  Turns schedule
  Automation

## Slide 6: Surface to Underground Actions Where Flow Quantification is Beneficial
Deeds
Segregations
Share statements
Change applications

## Slide 7: So...When is Water Not Wet?
When water rights actions fail to adequately address distribution consequences

## Slide 8: Distribution Accounting Models
https://waterrights.utah.gov/wcat/ListModels.asp