## Slide 1
Cedar Valley/ Northern Utah Valley
July 9, 2013

## Slide 2: Agenda
Background
Groundwater Hydrology
Current Conditions
Water Rights
Proposed Draft Policies
Monitoring Safe Yield

## Slide 3: Area
Cedar Valley
Northern Utah Valley

## Slide 4: Recent Studies
USGS – Hydrology of the Northern Utah Valley (2009)
UGS – Hydrogeology and Simulation of Groundwater flow in Cedar Valley (2012)

## Slide 5: Previous Meeting
1995 – Utah Valley and Cedar Valley
  Groundwater Management Plans
2004 – Cedar Valley
  Cedar Valley Groundwater Policy
  Filings transferring into Cedar Valley will be held

## Slide 6: Previous Meeting
2010 – Northern Utah Valley
  Presented Data from USGS Study & water rights
  Interim Policy
    Applications which represent a new groundwater withdrawal from the Northern Utah County Groundwater Management Area filed after September 30, 2010, will be held
2013 – Cedar Valley
  Presented Data from UGS Study & water rights

## Slide 7: Hydrology

## Slide 8: Water Resources
Area 54
  Recharge 26,000 ac-ft/year
  Cedar Pass Underflow 10,000 ac-ft/year
  Mosida Hills Underflow 4,700 ac-ft/year
Area 55
  Recharge 145,000 ac-ft/year

## Slide 9: Actual Use
Area 54
    Wells 6,700 ac-ft/year
    Drains & Springs 3,700 ac-ft/year
    Total 10,400 ac-ft/year
Area 55
    Wells 68,600 acft
    Drains & Springs 69,000 acft
    Total 137,600 ac-ft/year

## Slide 10: Hydrology
Actual Use: 10,400 acft
Actual Use: 137,600 acft

## Slide 11: Potential Withdrawal
Area 54
    West 19,500 ac-ft/year
    East 20,000 ac-ft/year
    Total 39,500 ac-ft/year
Area 55
    Total 245,000 ac-ft/year
    Approved and Perfected Water rights

## Slide 12: Hydrology
Potential use: 39,500 acft
Potential Use: 245,000 acft

## Slide 13: Area 54
Recharge, Potential and Actual Use
Recharge 26,000 ac-ft/yr
Potential Use 39,500 ac-ft/yr
Difference -13,500 ac-ft/yr
Actual Use 10,400 ac-ft/yr
Difference 15,600 ac-ft/yr

## Slide 14: Area 55
Recharge, Potential and Actual Use
Recharge 145,000 ac-ft/yr
Potential Use 245,000 ac-ft/yr
Difference -100,000 ac-ft/yr
Actual Use 137,600 ac-ft/yr
Difference 7,400 ac-ft/yr

## Slide 15: Area
Cedar Valley
Northern Utah Valley
Recharge: 145,000 acft
Potential Use: 245,000 acft
Difference: -100,000 acft
Actual Use: 137,600 acft
Difference: 7,400 acft
Recharge: 26,000 acft
Potential Use: 39,500 acft
Difference: -13,500 acft
Actual Use: 10,400 acft
Difference: 15,600 acft

## Slide 16: Proposed Policies
Effective date of this proposed policy will be the date this plan is implemented by the State Engineer.
30-day comment period.

## Slide 17: Proposed Policies
All areas will remain closed to new consumptive appropriations
All pending applications representing a new withdrawal of groundwater in area 55 (that portion within the plan area) and 54 East filed after September 30, 2010 are subject to this plan.

## Slide 18: Area
Cedar Valley
Northern Utah Valley

## Slide 19: Proposed Policies
Pending applications in area 55 (that portion within the plan area) and all of area 54 filed prior to September 30, 2010 will be evaluated on their individual merits.

## Slide 20: Proposed Policies
Surface water rights may not be changed to underground
  Unless:
    Replace Spring/Drain
      Report required
    Aquifer Storage and Recovery
    Within area 54 West
      Heretofore and hereafter diversions within 54 West
    Canyon Areas

## Slide 21: Area
Cedar Valley
Northern Utah Valley

## Slide 22: Proposed Policies
Existing groundwater rights may only be moved within the water right area in which it is currently approved. An exception is made for rights within the Central Zone defined in this plan. All change applications will be evaluated on their individual merits.

## Slide 23: Proposed Policies
The 2004 policy amendment limiting transfers of groundwater into Cedar valley is rescinded. However, transfers will be limited to rights with an existing approved groundwater point of diversion in the 54 Area.

## Slide 24: Area
Cedar Valley
Northern Utah Valley

## Slide 25: Proposed Policies
Groundwater transfers between water right areas will not be approved unless:
  Point of Diversion is within the Central Zone (2 mile buffer) as of June 4, 2013 and,
  Hereafter point must remain in the Central Zone

## Slide 27: Proposed Policies
Timpanogos Cave National Monument Protection Zone

## Slide 29: Safe Yield
Area 55 145,000 ac-ft/year
Area 54 26,000 ac-ft/year
Water Use Reporting
  100 ac-ft/year
  Install, operate, maintain, report
  Notices to be sent
Continued Adjudication Efforts

## Slide 30: Questions?
30 Day Comment Period
Address:
Utah Division of Water Rights
Teresa Wilhelmsen
1594 W. North Temple, Suite 220
PO Box 146300
Salt Lake City Utah 84114