## Slide 1: Aquifer Storage & Recovery Pilot Projects
Paul Inkenbrandt

## Slide 2
The Weber River Basin Aquifer Storage and Recovery Pilot Project
  Hurlow and others
  Surface application of water to recharge aquifer
  https://ugspub.nr.utah.gov/publications/special_studies/SS-136/ss-136_booklet.pdf
Cache Valley Aquifer Storage and Recovery - Phases I and II
  Inkenbrandt and Thomas
  https://ugspub.nr.utah.gov/publications/open_file_reports/OFR-615.pdf
Aquifer Storage and Recovery in Millville, Cache County, Utah
  Inkenbrandt
  Injection of water to recharge aquifer
  https://ugspub.nr.utah.gov/publications/reports_of_investigations/ri-275.pdf
Background- Experience

## Slide 3
Questions to answer with a pilot study:
Impact to other water rights?
  Quantity?
  Quality?
Where will the water go?
  Aquifer of interest
  Some person’s basement?
Change in groundwater chemistry?
  What is the baseline chemistry?
  Will you mobilize contaminants?
Amount added, extracted, and recovered?
Background- Questions you should address

## Slide 4
Steps for a successful pilot study:
Draft Design of Pilot Test
Compile existing information
Meet with regulators
Measure background conditions
Modify and build infrastructure
Conduct pilot test
Measure recovery conditions
Examine and share results
Background- Outline

## Slide 5
Find an adequate place for ASR
  Availability of recharge water
  Location to recharge water
  Location to recover water
Determine method of delivery
  Injection
  Surface application
Determine quantity of water to use in pilot test
  enough to measure changes
  unique to each situation
  may depend on water availability
Draft Design of Pilot Test
Good Guidance: http://www.ngwa.org/Advocacy-Awareness/Documents/BSP26-ASR.pdf
A feasibility study is often necessary

## Slide 6
Compile existing information
Compiling existing info will tell you what data you have and help you figure out what data you will need
Existing Studies
UGS Online Publications https://geology.utah.gov/map-pub/publications/
USGS Online Publications https://pubs.er.usgs.gov/
Utah Water Rights Online Publications https://www.waterrights.utah.gov/techinfo/default.asp
Water Chemistry Data
EPA and USGS https://www.waterqualitydata.us/portal/
Water Level Data
UGS https://apps.geology.utah.gov/gwdp/
USGS https://maps.waterdata.usgs.gov/mapper/index.html
Water Well Data
Utah Division of Water Rights WRPOD file https://waterrights.utah.gov/gisinfo/wrcover.asp

## Slide 7
Compile existing information
Water Well Data
Utah Division of Water Rights WRPOD file https://waterrights.utah.gov/gisinfo/wrcover.asp
Water Level Data
UGS https://apps.geology.utah.gov/gwdp/
USGS https://maps.waterdata.usgs.gov/mapper/index.html

## Slide 8
Compile existing information
Water Well Data
Utah Division of Water Rights WRPOD file https://waterrights.utah.gov/gisinfo/wrcover.asp

## Slide 9
Compile existing information

## Slide 10
Meet with regulators
Purpose = inform regulators of your intentions
you need permission to conduct a pilot test
Pilot test needed for a permit (most cases)
The public works official and the scientists or engineers conducting the study should start by meeting with:
  Utah Division of Water Rights (73-3b-201j)
  Utah Division of Water Quality

## Slide 11
Injection well:
  Utah Underground Injection Control (Class V ASR Well)
Public water supply:
  Utah Division of Drinking Water
Also the Utah Division of Water Resources is interested in and sometimes supports these projects
Meet with regulators

## Slide 12
Measure background conditions
Redox State
  Best measured with
    pH,
    dissolved oxygen, and
    oxidation-reduction potential
  Indicates if ions will dissolve or precipitate
  Think Flint Michigan

## Slide 13
GW Flow
Notable contaminants
  Arsenic, lead, uranium and other metals
  Nitrogen and other nutrients
Measure background conditions

## Slide 14
Measure background conditions
General Chemistry
  Field parameters:
    Conductivity
    pH
  Ca, Mg, Na, K,
  Cl, HCO3, SO4
Good for:
  models
  detection of changes
  comparison to other water

## Slide 15
Stable Isotopes
  Inexpensive and easy to use
  calculates mixing
  can infer temperature of recharge
Measure background conditions

## Slide 16
Groundwater Levels
Higher groundwater can mobilize contaminants previously in the unsaturated zone
cause flooding or other shallow groundwater hazards
Measure background conditions

## Slide 17
Modify and build infrastructure
Notes: Delivery Method
Volume Measurement
Sub-aqueous injection point

## Slide 18
Aquifer storage and recovery can treats the aquifer like a reservoir.
Saves “bubble” of spring water in the aquifer.
Conduct pilot test & Measure recovery conditions

## Slide 19
Injection
Pump
Conduct pilot test & Measure recovery conditions

## Slide 20
Conduct pilot test & Measure recovery conditions

## Slide 21
Conduct pilot test & Measure recovery conditions

## Slide 22
6/7/2016 Alder well nitrate concentration is 8.6 mg/L
Conduct pilot test & Measure recovery conditions
Notes: 6/7/2016 Alder well nitrate concentration is 8.6 mg/L

## Slide 23
Modeling - Injection

## Slide 24
Modeling - Nitrate

## Slide 25
Summary
Summary:
Background data are essential
Key things to measure can be measured in the field (pH, ORP, conductivity, dissolved oxygen)
Good well coverage is important (may need a monitoring well)
Stable isotopes can be useful for calculating mixing

## Slide 26
Questions?

## Slide 28
Background - Nitrate
Distribution of septic systems in the area.
High concentration of systems up gradient of Glenridge Well
GW Flow